## Slide 1
The on board LED will turn green when you press the space bar. Note the yellow flash that indicates the event happened. The “o” key will turn the LED off.
Can you chance the color?
Lab 1: Turn LED On
Lab 2: Flash LED (Blink Lab)
The on board LED will flash green when you press the space bar.
Can you chance the speed that the LED flashes? Note that the wait can contain a decimal value like 0.1 or 0.05.
Advanced – why is there a limit on how fast the LEDs flash? (hint – is the command stream is a limiting factor)

## Slide 2
We can change just the right or left LEDs. Can you make both turn red, then the left green, then the right blue?
Lab 3: Left and Right LEDs
Lab 4: Conditional Ping
Robots can sense the world around them and then change their behavior. Can you make the color change based on what is in front of the robot?
How is this lab like a stoplight? What does green show?

## Slide 3
Green means there is nothing in front of us. It means go forward. But then block is detecting an obstacle in from of us. Lets turn the different LEDs on to show that we need to turn to avoid a crash!
Lab 5: Green Means Go!
Lab 6: Rainbow Colors
What if you wanted your distance to change the color to more than two colors? Here is an example that uses the and block to test if the sensor is within a range.
Hint: to write this faster, use the duplicate (right click) to copy the if/then block.
How many colors can you make?

## Slide 4
The mBot has a light sensor on the top. The program above will change the LED color based on how much light is hitting the robot.
Do you think the LEDs will change the value of the light sensor?
7: Light Sensor Lab
Lab 8: Line Follower Lab
The mBot has a two line followers on the bottom of the robot. There are robot blocks that return true or false if the robot is above a white or black object. Run the program above and note when the blue LEDs on the mBot turn on and off. How far above white paper do the sensors need to be to work?

## Slide 5
Before we do this lab, put your robot on the floor! This way it will not drive off the table and crash.
This lab requires your robot to drive in a square. You must press “g” for it to start. The space bar will stop both motors.
Lab 9: Drive in a Square
Lab 10: Collision Avoidance
Make the robot go forward until it gets close to an obstacle. Then turn right.
Can you make the robot back up first and then turn when there is an obstacle in front of it?